SPECIFICATIONS: tellurus™ HMI

Display Features

Pump Specifications

# Text boxes

®

- a-Si Active Matrix LCD

- 1300 cd/m2 High-bright Backlight

- Direct Sunlight Readability

- 700:1 High Contrast Ratio

- 80º Viewing Angle

- Ambient Light Sensing

- Multi-point Glass Resistive Touchscreen

- Gloved Operation In Water Spray Environment

- Chemically Strengthened Glass Micro-sheet

- Impact Resistant

- Circular Polarizing Filter

- Anti-reflective Coating

- Dry-Film Optical Bonding

Graphic Architecture

- 24-bit Truecolor

- Intel® HD Graphics DX11, Open GLE ES 3.0

Embedded Controller

- Intel®  Atom®  Dual-core Processor @ 1.75GHz

- 2MB L2 cache

- 2GB DDR3 DRAM (expandable to 8GB)

- 8GB SLC SATA SSD (expandable to 128GB)

- Real-Time ClockWaterous Five-Year Limited Warranty

OS Software

- WindRiver® Linux 5.0

- Intel® IDP 2.0 WAN Security

- McAfee® Embedded Control

Environmental Protection

- -40C to +85C Operating Temperatures

- Water resistant to IP67

- Vibration to MIL-STED-810G for Ground Based Motor Vehicles

Powered By

Device Connectivity

- 2 x Ethernet IEC 61067–2–101, 4-pin, M12, 10/100 Base-T

- Secure Networking VPN: IPSEC/PPTP/L2TP

- Sealed M12 Mini Hi-Speed USB 2.0 Host Port

- Bluetooth 4.0 With BLE Support

- Integrated 802.11 a/b/g/n WiFi, Host-AP and Client Mode Support

- Open Mobile Alliance Device Management (OMA DM)

- WebIF Web-based Configuration

- Accelerometer

- 12 Channel GPS Receiver (optional)

- WiFi dual Band / GPS Antenna (optional)

- GSM/GPRS/CDMA 3G/4G LTE Cellular Modem (optional)

Power Supply

- 9-32VDC Transient Protected

- Power Consumption < 15W

®

Intel® Gateway Solutions for the Internet of Things (IoT)

10.4-inch Diagonal Screen Size

SVGA (1024 X 768) Resolution

7.0-inch Diagonal Screen Size

WSVGA (1024 X 600) Resolution

15.0-inch Diagonal Screen Size

SVGA (1024 X 768) Resolution

TELLURUS™ 7” HMI	TELLURUS™ 10” HMI	TELLURUS® 15” HMI