SPECIFICATIONS – industrial: Model tml
Your High-Performance Industrial Transmission

The Waterous TML is a full-torque, split-shaft power take-off with counter-enginewise rotation. The TML has outputs to 150 HP (112kW) and thru torque to 9100 ft. lb (12,400 N•m). The TML also has output to the front, rear or both and has five available ratios.

Case:

High-tensile gray iron

Driveline:

Standard:

- 1-3/4-10 SAE spline, 4100 ft-lb torque rating

Optional:

- 2-10 SAE spline, 6100 ft-lb torque rating

- 2-38T involute spline, 9100 ft-lb torque rating

Bearings:

Oil lubricated ball bearings throughout.

Output Shaft:

- 1-3/8 spline with yoke

- Output to front, rear or both

- Front output rotation - clockwise

- Rear output rotation - counterclockwise

Gears:  Constant mesh helical, alloy steel.  All gears are crown shaved, carburized and hardened.  The bores are precision ground.

Tachometer and Speed Connection – Mechanical Drive Design:

Standard:

Without tachometer or speedometer

Optional:

- Tachometer only

- Speedometer only (not available with 2 in. driveline)

- Tachometer and Speedometer (not available with 2 in. driveline)

Electric Shift:

Dependable in-cab control eliminates mechanical linkages, and simplifies shifting operation.

Parking Brake:

Bendix Duo-Duty, available as follows:

1-3/4-10 SAE Driveline

- 9 x 3 for 1500 series U-joints

- 12 x 3 for 1600 series U-joints

2-10 SAE Driveline

- 12 x 3 for 1700 series U-joints

2-38T Involute Driveline

12 x 3 for 1700 series U-joints.

| Ratio | Output Shaft Speed (RPM) |
| --- | --- |
|  | 200 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 |
| 0.71 | 45 | 80 | 140 | 150 | 150 |  |  |  |
| 0.88 | 40 | 75 | 130 | 145 | 150 | 150 |  |  |
| 1.04 | 35 | 70 | 120 | 140 | 145 | 150 | 150 |  |
| 1.29 | 30 | 65 | 110 | 135 | 140 | 150 | 150 | 150 |
| 1.59 | 27 | 58 | 95 | 127 | 137 | 147 | 150 | 150 |

When you purchase Waterous equipment, not only do you get quality products, you get quality service. Our expert service technicians are the best in the business and they are always happy to answer any service questions you might have.

Sales/Applications Assistance	Service Assistance
Phone: 651-450-5234 (Press 3) 	Phone: 651-450-5200
pumpsales@waterousco.com 	Fax: 800-488-1228

service@waterousco.com

# Text boxes

Specifications:

Optional Equipment:

Industry-Leading Sales and Support

Ratio Horsepower Ratings: