SPECIFICATIONS – floto-pump®
Flows up to 140 GPM (530 l/min) and Pressures to 170 PSI (12 bar)

Waterous Floto-Pumps® are available in two models, Standard and High Pressure (Forest Service).Weighing only 42 lbs. (19.1 kg), the pump is easily carried by ONE person. The Floto-Pump also comes with a One-Year Limited warranty and is CE marked*.

| Floto-Pump® Performance |  |
| --- | --- |
| Model | Max Flow (GPM) | Max Flow (L/min) | Max Flow (L/sec) | Max Pressure (PSI) | Max Pressure (bar) | Max Pressure (kPa) | Max Pressure (MPa) |
| Standard | 140 | 530 | 8.75 | 105 | 7 | 700 | 0.7 |
| High Pressure | 60 | 230 | 3.75 | 170* | 12* | 1200* | 1.2* |

*High Pressure Floto-Pump throws a stream of water over 85 feet (26 m) at 170 PSI (12 bar, 1200 kPa, 1.2 MPa)

Pump Features:

# Text boxes

The Waterous Floto-Pump® was originally developed to meet the rugged demands of the United States Forest Service (USDA Forest Service Qualified Spec. S100-00275) and is now also used for marine service, dewatering, pool maintenance, environmental clean-up and irrigation.

The Floto-Pump is backed by a Waterous One-Year Limited Warranty.

For details on Waterous Condition of Sales, refer to F-2190, Conditions of Sales located on the Waterous web site at www.waterousco.com or by contacting Waterous.

Pump Specifications

Casing:

Anodized Aluminum

Impeller:

Bronze impeller (aluminum impeller with Ni-resist wear rings on HP model)

Shaft Seal:

Face-type mechanical seal is standard. No adjustment required.

Discharge:

1-1/2 in. NH, 1-1/2 in. NPSH or BSP thread available

Other Standard Equipment:

- Built-in intake screen

- Water-resistant air cleaner and muffler

Engine Specifications

U.S. Motor Power ``Power Bee''

- 8 horsepower, 8.20 cu. in. (134cc) displacement, air-cooled

- L series model 82029, one cylinder, two-cycle

- Recoil starter with “D” handle

- Pressure carburetor with integral fuel pump

- Solid-state ignition

- Hard chrome-plated cylinder bore

- Ball bearing-supported crankshaft

- Roller bearing-equipped connecting rod

- Uses unleaded gasoline and oil mixed

- Automatic float controlled throttle

Miscellaneous:

Fuel Tank:

5 quart (4.7 liter) capacity (1 to 1-1/2 hr running time)

Float Assembly:

High-density polyethylene shell filled with polyurethane foam (closed cell)

Accessories:

- 1-1/2 in. Forestry fire hose

- Nozzle

- Spanner wrench

Dimensions and Weight

| Length (in/mm) | Width (in/mm) | Height (in/mm) | Weight (lb/kg) |
| --- | --- | --- | --- |
| 28 (711) | 16 (406) | 20 (508) | Dry | 42 (19.1) |
|  |  |  | Shipping | 51 (23.2) |

Performance Curve

RAISING THE BAR ON INNOVATION, RELIABILITY AND SERVICE.

Industry Leading Sales and Support

When you purchase equipment, not only do you get quality products, you get quality service. Our expert service technicians are the best in the business and they are always happy to answer any service questions you might have.

Sales/Applications Assistance	Service Assistance
Phone: 651-450-5234 (Press 3) 	Phone: 651-450-5200
pumpsales@waterousco.com 	Fax: 800-488-1228

service@waterousco.com