SPECIFICATIONS – S100D-1500
What’s all the noise about? Waterous Silences the Competition.

The Waterous S100D-1500 Fire Pump meets the NFPA Rating of 1500 GPM without the need for a pump transmission.  After an evaluation of our product by Chelsea, Waterous received instant approval to use the Chelsea 870-series PTO with a 200% ratio and an Allison EVS3000 Series Transmission (side/top PTO opening). The max engine speed required for this application is only 2000 RPM.

| S100-D Pump Performance |
| --- |
| GPM | L/min | L/Sec | PSI | Bar | kPa | MPa |
| 750 | 3000 | 50 | 250 | 10 | 1000 | 1.0 |
| 1050 | 4000 | 65 | 200 | 14 | 1400 | 1.4 |
| 1500 | 6000 | 100 | 165 | 11 | 1100 | 1.1 |
| 1500 | 6000 | 100 | 150 | 10 | 1000 | 1.0 |

Key Factors:

- Pump weighs only 220 pounds

- No Pump Transmission

- Max Engine Speed Required: 2000 RPM

Pump Features:

Optional  Equipment (See Next Page)

SPECIFICATIONS: VEHICLE-MOUNTED: mODEL S100D-1500

Pump Specifications:

Pump Body:

Cast in ductile iron. Double stripping edge volute minimizes radial forces at all flow rates.

Intake:

8” Victaulic

Discharge:

5 inch ANSI flange or an optional 21st Century Manifold (4 in. end flanged manifold with (8) 2-1/2 in. side pads) or an optional 5 in. ANSI to 4 in. ANSI adapter.

Impeller:

Bronze impeller, balanced mechanically and hydraulically for vibration-free operation and flame-plated to assure longer life despite the presence of abrasives in the water supply.

Impeller Shaft and Seal:

Stainless steel shaft and impeller nut with spring-loaded mechanical shaft seal. Self-adjusting mechanical seal eliminates leakage and routine maintenance.

Wear Rings:

Bronze labyrinth-type (reverse-flow) replaceable wear rings increase pump life and keep maintenance costs to a minimum.

V-ring:

Located on the impeller shaft between mechanical seal and transmission oil seal, the V-ring provides added protection by keeping water and foreign matter out of the bearings.

Oil Seals:

Single lip, spring-loaded design for lubrication seal and additional bearing protection from dirt and water.

Options:

The accessories below are available for Waterous S100 pumps. For detailed information about these accessories, request each specification sheet by number.

Primer

Select an electric rotary vane priming system. Separately Mounted. See Priming Systems, F-2418

Pressure Control Systems

Intake Relief Valves - Separately Mounted

The Waterous intake relief valve is designed to dump excess pressure from the inlet side of the pump. See Intake Relief Valves, F-2192.

21st Century Manifold

The 21st Century Manifold is designed to be mounted on the S101 discharge flange. It can be orientated for top or side-mount control panels. Flange arrangements and spacing allows for organized horizontal layout plumbing of all discharges and eases the layout of the panel by the apparatus builder. See 21st Century Manifold, F-2478.

Corrosion Protection

Waterous offers replaceable zinc intake screens and anodes  to provide corrosion protection. These items are designed to sacrifice the zinc element to galvanic corrosion. Without this protection, galvanic corrosion may damage the iron pump body and fittings.

Overheat Protection Manager

The OPM consists of an illuminated warning light on the operator's panel whenever the pump approaches an overheat condition. See OPM, F-2422

Drain Valves

Drains all points of the pump simultaneously with the operation of a single control. See Drain Valves, F-1158

Total Protection Package (TPP-5)

The Total Protection Package is a comprehensive warranty that increases your standard warranty to include labor expenses to dismantle, remove and reinstall covered products or parts, F-2626.

# Text boxes

- Ductile iron pump body

- Bronze, flame-plated,  mechanically and hydraulically balanced impeller

- Stainless steel impeller shaft

- Bronze labyrinth-type (reverse flow) wear rings for increased pump life

- Self-adjusting mechanical seal

- 8-inch Victaulic® Intake

- 5-inch ANSI Flange Discharge

- Aluminum bearing housing with deep groove, anti-friction ball bearings for support and proper alignment of the impeller shaft assembly.

Warranty

Waterous Five-Year Limited Warranty.

Conditions of Sales

For details on Waterous Conditions of Sales, refer to F-2190, Conditions of Sales located on the Waterous web site at www.waterousco.com or by contacting Waterous.

- Priming System

- Pressure Control Systems – Discharge and Intake Relief Valves

- Corrosion Protection – Zinc Intake Screens and Anodes

- Overheat Protection Manager

- Drain Valves

- 21st Century Manifold

- Five-Year Limited Warranty with Total Protection Package (TPP-5)

RAISING THE BAR ON INNOVATION, RELIABILITY AND SERVICE.

Industry Leading Sales and Support

When you purchase equipment, not only do you get quality products, you get quality service. Our expert service technicians are the best in the business and they are always happy to answer any service questions you might have.

Sales/Applications Assistance	Service Assistance
Phone: 651-450-5234 (Press 3) 	Phone: 651-450-5200
pumpsales@waterousco.com 	Fax: 800-488-1228

service@waterousco.com