SPECIFICATIONS – Transmissions: Model T

| Drive | Type | Model | Helical Gear Data | Available Bellhousings | Power Capability (See Note) | Available Ratios |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Pitch | Face Width | Center Distance | Housing Adapter | For Clutch No. |  |  |
| Direct Engine Mount for SAE Flywheel for Driving Over Center Type Clutch per SAE J620 | Two-Gear Without Hydraulic Clutch | Medium Duty T (MDT) | 12 | 1-1/2 in. | 4.589 in. 116.56 mm | SAE 3 or 4 | 10 | Equipment Requiring Up to 65 HP (48.5 kW) | 1.44, 1.62, 1.97, 2.14, 2.33, 2.55, 2.79, 2.93, 3.40, 4.00, 4.79 |
|  |  |  |  |  |  | SAE 4 | 8 |  |  |
|  |  |  |  |  |  | SAE 3 | 11-1/2 |  |  |
|  |  |  |  |  |  | SAE 5 | 6-1/2 |  |  |
|  |  | Heavy Duty T (HDT) | 8 | 1-5/8 in. | 4.589 in. 116.56 mm | SAE 2, 3 or 4 | 10 | Equipment Requiring Up to 150 HP (111.9 kW) | 1.16, 1.38, 1.56, 1.65, 1.76, 1.88, 2.14, 2.45, |
|  |  |  |  |  |  | SAE 2 or 3 | 11-1/2 |  |  |
|  |  | TA | 12 | 1-1/2 in. | 4.50 in 114.30 mm | SAE 4 | 8 | Equipment Requiring Up to 65 HP (48.5 kW) | 2.00 |
|  |  |  |  |  |  | SAE 5 | 6-1/2 |  |  |

Note: Power capability list is for general guidelines only. Contact Waterous Applications Manager for your specific requirements.

Input Rotations:

- Clockwise or counter clockwise (All Models Except TA)

- Clockwise (TA Only)

Case Mounting:

- Vertical, Horizontal (Left or Right), Inverted  (All Models Except TA)

- Vertical (TA Only)

Tachometer:

- Optional Mechanical Gear Drive (All Models Except TA)

- Not Available on TA

Optional Drive Plates:

No. 6-1/2, 8, 10 or 11-1/2 available

When you purchase Waterous equipment, not only do you get quality products, you get quality service. Our expert service technicians are the best in the business and they are always happy to answer any service questions you might have.

Sales/Applications Assistance	Service Assistance
Phone: 651-450-5234 (Press 3) 	Phone: 651-450-5200
pumps@waterousco.com 	Fax: 800-488-1228

service@waterousco.com

SPECIFICATIONS – Transmissions: Model T

# Text boxes

Available Models:

Specifications:

Industry-Leading Sales and Support