SPECIFICATIONS – accessories: Intelligent caf selector (ICS) 
Elevates CAFS operations and functionality to a whole new level.

ICS (Intelligent CAF Selector) for Elkhart Brass Unibody series electric valves integrates with Waterous compressed air foam systems to provide one-button control of any CAF discharge. With ICS equipped Waterous CAFS, producing CAF is extremely simple yet retains the flexibility to produce the right foam at each discharge.

ICS is an integrated CAF discharge controller for any Waterous Eclipse™, Platinum or Silver Series PTO or Integrated Crossmount CAFS equipped with an Advantus® Foam System or Aquis™ Foam Proportioner. ICS provides control of a 1-1/2” to 8” Elkhart Brass Unibody electric water valve and a standard 12-24 VDC solenoid air valve.

The patented direct absolute valve position feedback, only available from the Unibody electric valve, allows the ICS operator to easily program and select from three CAF modes; Wet, Medium and Dry or water and/or air only. ICS simplifies the pump panel by including all discharge controls and a discharge pressure display in one easy to use, easy to see, easy to program device.

| Model | UICS-2 |
| --- | --- |
| Part Number | 08899190 |
| Supply Voltage | 12-24 VDC |
| Supply Current | 15 Amp Max |
| Water Valve Compatibility | Unibody Electric 1-1/2” to 8” |
| Air Valve Compatibility | 24 VDC Max, 2 Amp Max |
| Enclosure | Positive Pressure Vented Aluminum |
| Bezel | Textured Black with Optional Chrome Trim Ring |
| Display | All High Intensity with Auto Dim |
| Valve Position | 10 LED Position Plus 1 LED Closed |
| Pressure | 8 Character LCD Programmable for PSI or KPA |
| CAF Mode | 8 Character LCD Status Plus 1 LED On |

Contact Elkhart Brass Manufacturing directly @ 1-800-346-0250 to order your ICS.

When you purchase Waterous equipment, not only do you get quality products, you get quality service. Our expert service technicians are the best in the business and they are always happy to answer any service questions you might have.

Sales/Applications Assistance	Service Assistance
Phone: 651-450-5234 (Press 3) 	Phone: 651-450-5200
pumpsales@waterousco.com	Fax: 800-488-1228

service@waterousco.com

SPECIFICATIONS – accessories: intelligent caf selector (ICS)

NOTE: Information on this specification sheet was derived from Elkhart Brass Manufacturing information on the ICS.

Elkhart Brass Manufacturing Company, Inc., 1302 W. Beardsley Avenue, Elkhart, Indiana, 46415  www.elkhartbrass.com.

# Text boxes

Description:

Industry-Leading Sales and Support

Ordering Information

ICS Wiring Diagram

Specifications: