SPECIFICATIONS – motor pumps: E500 series
Specialized Pump Capabilities for Specialized Attack Vehicles

The E500 Series Motor Pump is specifically designed for mounting on specialized attack vehicles. The diesel-powered motor pump combines the muscle of Waterous vehicle-mounted pumps with the convenience of its own power source. Available in two models: E501 or E511:

| E500 Pump Performance |
| --- |
|  | FLOW | PRESSURE |
|  | GPM | l/min | l/sec | PSI | bar | kPa | MPa |
| Max Flow | 275 | 1100 | 18 | 50 | 3.5 | 350 | .350 |
| Max Pressure | 50 | 200 | 3 | 400 | 28 | 2800 | 2.8 |

Pump Specifications:

Intake:

E501-C: 	2 inch female NPT

E511-C:	3 inch female NPT (Optional 3 inch Victaulic Adapter)

Discharge:

E501-C:	1-1/2 inch female NPT

E511-C:	2 inch female NPT (Optional 2 inch Victaulic Adapter)

Volute Body and Head:

High-strength aluminum alloy protected by a proprietary dual anodizing and sealing process for superior corrosion protection and resistance to acids and alkaline solutions.

Impeller:

High-strength, corrosion-resistant bronze, fully enclosed, double-hubbed to balance hydraulic thrust, mechanically balanced to eliminate vibration.

Impeller Shaft:

Integral driven gear and shaft made of hardened steel, nickel-plated for wear and corrosion resistance.

Wear Rings:

Long wearing bronze. Easy to replace when required to restore original pump efficiency.

Drive Shaft and Gear:

High-strength stainless steel shaft and a heat-treated ductile iron gear.

Shaft Seal:

Spring-loaded mechanical type. Wear and heat resistant silicon-carbide.

Gear Case:

Two-gear speed increaser utilizing high-strength aluminum alloy case. Helical cut gears for reduced wear and noise and anti-friction bearings throughout.

Dimensions and Weights:

| Model | Length (in/cm) | Width (in/cm) | Height* (in/cm) | Weight (lb/kg) |
| --- | --- | --- | --- | --- |
| E501-C | 34.39 (87.4) | 20.8 (52.8) | 25 (63.5) | 252 (115) |
| E511-C | 35.28 (89.6) | 20.8 (52.8) | 25 (63.5) | 237 (108) |

Engine Specifications:

Engine:

Kubota, Model D902-E3B, Super Mini Series, in-line 3-cylinder, water-cooled, naturally aspirated delivering a maximum output of 24.8 hp (18.5 kw) @ 3600 RPM, 54.8 cu. in. (898 cc) displacement, 4-cycle, diesel fueled.

Lubrication:

Pressure fed with spin on filter.

Starter:

12-14 volt, 1.2 kW

Emission Regulation:

Tier 4

Alternator:

12 VDC, 40 AMP

Options and Accessories:

Priming System:

The priming system consists of either a Waterous' hand or electric primer shipped loose for remote mounting.

Exhaust System:

Spark Arrestor

Control Panel:

- New Control Module - Allows the operator to change operating parameters electronically with a touch of a button.

- No Panel Option

motor pumps: E500 series

Performance Curves:

# Text boxes

RAISING THE BAR ON INNOVATION, RELIABILITY AND SERVICE.

RAISING THE BAR ON INNOVATION, RELIABILITY AND SERVICE.

E501-C

E511-C