SPECIFICATIONS: Vehicle Mounted: cGVG
Meets NFPA 1901 for 750 GPM and NFPA 1902 for 500 GPM

The single stage CGVG pump configuration with special crosspipe intake allows for midship mounting of the CG Series Pump.

| CGVG Pump Performance |
| --- |
|  | FLOW | PRESSURE |
| Rating | GPM | l/min | l/sec | PSI | bar | kPa | MPa |
| NFPA 1901 | 750 | 3000 | 50 | 150 | 10 | 1000 | 1.0 |
| NFPA 1902 | 500 | 2000 | 30 | 150 | 10 | 1000 | 1.0 |

Pump Features

The S100 is backed by a Waterous Five-Year Limited Warranty.

For details on Waterous Conditions of Sales, refer to F-2190, Conditions of Sales located on the Waterous web site at www.waterousco.com or by contacting Waterous.

Optional Equipment (see next page)

SPECIFICATIONS: vehicle mounted: mODEL cgvg

Pump Transmissions

K Series

The K Series Transmission is normally used when a truck transmission mounted power take-off is selected as the pump drive.

Housing: Close-grained, gray iron

Gears: Helical, precision cut, crown shaved for proper load distribution and quiet operation.

WB Series

The “WB” series incorporates a high-strength involute tooth form chain designed to operate at high speeds and provides smooth, quiet transfer of power.C20 Series

The “C20” series transmission is supplied when the pump is to be midship mounted. Power from the truck's automatic transmission is transmitted to the pump.

Housing: High-strength aluminum

Chain: Morse HV®, high-strength involute chain

PA Series

PA Series transmission is normally used when a truck transmission mounted power take-off is selected as the pump drive. Designed for use with Allison transmissions with 10-bolt PTO.

Housing: High-strength aluminum

Chain: Morse HV®, high-strength involute chain

Pump Specifications

Casing:

Two-piece, vertically-split, high-tensile, close-grained gray iron, or bronze (optional).

Wear Rings:

Replaceable bronze wear rings to increase pump life and keep maintenance costs at a minimum.

Impeller:

Bronze impeller, double-hubbed specifically designed for the fire service and accurately balbanced for vibration-free running. Impeller with flame-plated hub is optional.

Impeller Shaft:

Stainless steel, heat treated and precisely ground to size. Supported by oil-lubricated ball bearings.

Bearings:

All bearings are oil-lubricated, ball-type, located outside the pump casing to accurately align and support the impeller shaft assembly. Ball bearings are deep-groove type designed to carry both radial and axial thrust.

Shaft Seal:

Self-adjusting and wear-resistant mechanical seal is standard.

Flinger Ring:

Located on impeller shaft between stuffing box and bearing housing as added protection in keeping water and foreign matter out of bearings.

Accessories & Optional Equipment

The accessories below are available for Waterous CGVG pumps. For detailed information about these accessories, request each specification sheet by number.

Primer

Select an electric rotary vane primer for fast, reliable priming. F-2418

Pressure Control Systems

Discharge Relief Valve

Simple ON-OFF control permits placing the system in or out of operation in seconds. See Relief Valve, F-897.

Intake Relief Valves

The Waterous intake relief valve is designed to dump excess pressure from the inlet side of the pump. See Intake Relief Valves, F-2192.

Intake Fittings

Available in 4, 4-1/2, 5 or 6 inch sizes. Each fitting offers a choice of 2-1/2 inch or 3 inch openings for auxiliary suction piping.Corrosion Protection

Waterous offers replaceable zinc intake screens and anodes to provide corrosion protection. These items are designed to sacrifice the zinc element to galvanic corrosion. Without this protection, galvanic corrosion may damage the iron pump body and fittings.

Overheat Protection Manager

The OPM consists of an illuminated warning light on the operator's panel whenever the pump approaches an overheat condition. F-2422

Drain Valves

Drains all points of the pump simultaneously with the operation of a single control. F-1158

Discharge Valves

The following Waterous ball-type discharge valves are available: 2-1/2 inch, 3-1/2 inch, rack and sector push-pull, worm gear and electric. Chrome- plated brass ball and hydraulically-balanced seal assembly standard. See Discharge Valves, F-1161.

Tachometer

Tachometer drive available; operates at 1/2 input shaft speed.

# Text boxes

- Two-piece, vertically-split, high-tensile, close-grained gray iron, or bronze (optional).

- Self-Adjusting Mechanical Seal

- Replaceable bronze wear rings

- Stainless steel impeller shaft supported by oil-lubricated ball bearings.

- Bronze, double-hubbed impeller for smooth operation and longer life (Flame plating optional)

- 3” Flanged Discharge

- Rotation: Available in clockwise or counterclockwise rotation.

- Available with either threaded or Victaulic® intake connections. Threaded intake connections are available in three popular sizes. The CGV can also be used with a Victaulic® intake and discharge fittings for crash truck or fire boat use.

Warranty

Waterous Five-Year Limited Warranty

Conditions of Sales

For details on Waterous Condition of Sales, refer to F-2190, Conditions of Sales located on the Waterous web site at www.waterousco.com or by contacting Waterous.

- Priming System

- Pressure Control Systems – Discharge and Intake Relief Valves

- Corrosion Protection – Zinc Intake Screens and Anodes

- Overheat Protection Manager

- Drain Valves

- Discharge Valves

- Pneumatic  Shift

- Five-Year Limited Warranty with Total Protection Package (TPP-5)

- Tachometer drive, operates at ½ input shaft speed.

- Transmissions Available:

  - C20 Chain Drive (Split-Shaft)

  - P Series Chain Drive (PTO Driven)

  - K Series Gear Driven (PTO Driven)

  - WB Series Gear Driven (Split-Shaft)

RAISING THE BAR ON INNOVATION, RELIABILITY AND SERVICE.

Industry Leading Sales and Support

When you purchase equipment, not only do you get quality products, you get quality service. Our expert service technicians are the best in the business and they are always happy to answer any service questions you might have.

Sales/Applications Assistance	Service Assistance
Phone: 651-450-5234 (Press 3) 	Phone: 651-450-5200
pumpsales@waterousco.com 	Fax: 800-488-1228

service@waterousco.com

IL1526

IL1737