SPECIFICATIONS: Model CR/CRU High-flow pump
FOR ARFF, MUNICIPAL AND INDUSTRIAL APPLICATIONS

Waterous CR/CRU single-stage centrifugal high-flow pumps can be used in a multitude of applications. Whether used in aircraft fire fighting, moving large amounts of water for municipalities or flowing water for industrial applications, the CRU has the capabilities to get the job done.

| CR/CRU Pump Performance |
| --- |
|  | FLOW | PRESSURE |
| Model | GPM | l/min | l/sec | PSI | bar | kPa | MPa |
| CR | 2050 | 8000 | 130 | 250 | 17 | 1700 | 1.7 |
| CRU | 2640 | 10000 | 165 | 250 | 17 | 1700 | 1.7 |

Pump Features

Pump Specifications

SPECIFICATIONS: Model CR/CRU High Flow Pump

Accessories & Optional Equipment

The accessories below are available for Waterous CR pumps. For detailed information about these accessories, request each specification sheet by number.

Primer

Select an electric rotary vane primer for fast, reliable priming.

F-2418

Pressure Control Systems

Discharge Relief Valve

Simple ON-OFF control permits placing the system in or out of operation in seconds. See Relief Valve, F-897.

Intake Relief Valves

The Waterous intake relief valve is designed to dump excess pressure from the inlet side of the pump. See Intake Relief Valves,

F-2192.

Corrosion Protection

Waterous offers replaceable zinc intake screens and anodes to provide corrosion protection. These items are designed to sacrifice the zinc element to galvanic corrosion. Without this protection, galvanic corrosion may damage the iron pump body and fittings.

Overheat Protection Manager

The OPM consists of an illuminated warning light on the operator's panel whenever the pump approaches an overheat condition.

F-2422

Drain Valves

Drains all points of the pump simultaneously with the operation of a single control. F-1158

Discharge Valves

The following Waterous ball-type discharge valves are available: 2-1/2 inch, 3-1/2 inch, rack and sector push-pull, worm gear and electric. Chrome- plated brass ball and hydraulically-balanced seal assembly standard. See Discharge Valves, F-1161.

Pump Specifications

# Text boxes

- Single stage, vertically- split body constructed of gray iron (bronze optional)

- Bronze replaceable wear rings

- Bronze, mechanically and hydraulically balanced impeller

- Stainless steel impeller shaft

- Self-adjusting mechanical seal

- 8-inch flanged intake

- 5-inch Victaulic discharge

Warranty

Waterous Five-Year Limited Warranty

Conditions of Sales

For details on Waterous Condition of Sales, refer to F-2190, Conditions of Sales located on the Waterous web site at www.waterousco.com or by contacting Waterous.

CRU Model

Optional Equipment (See Next Page)

- Priming System

- Pressure Control Systems – Discharge and Intake Relief Valves

- Corrosion Protection – Zinc Intake Screens and Anodes

- Overheat Protection Manager

- Drain Valves

- Discharge Valves

- Discharge Positions:

- Available in 25° below horizontal, horizontal or vertical.

- Pneumatic  Shift

- Transmissions Available:

  - QA (10-1/2 inch offset) CR Pumps Only

    - Chain Driven

    - Gray-iron Case

    - 1:1 ratio

    - 1.750-10 SAE spline with Spicer 1550 Series End Yoke

  - QB (18-1/4 inch offset) CR Pumps Only

    - Chain Driven

    - Aluminum Case

    - 1:06 ratio

    - 1.750-10 SAE spline with SPL Series 90 End Yoke

  - QB (18-1/4 inch offset) CRU Pumps Only

    - Chain Driven

    - Aluminum Case

    - 1:072 ratio

    - 1.750-10 SAE spline with SPL Series 90 End Yoke

CR Model

RAISING THE BAR ON INNOVATION, RELIABILITY AND SERVICE.

Discharge:

5 inch (12.7 cm) Victaulic®

Discharge Positions:

Available in horizontal or vertical.

Bearings:

All bearings are oil-splash lubricated, anti-friction (ball-type), and located outside the pump casing to accurately align and support the impeller shaft assembly. Ball bearings are deep-groove or angular- contact type designed to carry both radial and axial thrust.

Drive:

CRQA Models Only - Direct drive with 1.750-10 spline for Spicer 1550 Series End Yoke.

CRQB/CRUQB Models – 1.750 SAE spline with SPL Series 90 End Yoke

Casing:

Gray iron (bronze optional)

Wear Rings:

Bronze replaceable wear rings to increase pump life and keep maintenance costs to a minimum.

Impeller:

Bronze, mechanically and hydraulically balanced to eliminate vibration.

Impeller Shaft:

Stainless steel, heat treated, ground to precise size and polished under shaft seal.

Seal Type:

Mechanical seal is standard (self-adjusting). Intake:

8 inch (20.3 cm) flanged

Industry Leading Sales and Support

When you purchase equipment, not only do you get quality products, you get quality service. Our expert service technicians are the best in the business and they are always happy to answer any service questions you might have.

Sales/Applications Assistance	Service Assistance
Phone: 651-450-5234 (Press 3) 	Phone: 651-450-5200
pumpsales@waterousco.com 	Fax: 800-488-1228

service@waterousco.com